## Slide 1: IoT Hardware & Firmware
Building an IoT Clock
By Liam Osman

## Slide 2: Agenda
IoT Recap
Hardware
  Voltage / Resistance / Current
  Breadboard and Connecting Pins
Firmware
  Definition
  Platforms
Board Setup
  Registration
  Circuit Building
Coding

## Slide 3: IoT Recap

## Slide 4: Internet of Things
  Network of physical objects or “things” that are embedded with sensors, software, and other technologies to collect and exchange data with other devices and systems over the internet.

## Slide 5: Examples of IoT Devices
Fitness tracking devices
Hospital call buttons
Smart light bulbs
Smoke Detectors (w/ internet)
Automatic traffic lights
Car computers (w/ internet)

## Slide 6: IoT Systems
Microcontrollers:
  Nordic Semiconductor nRF
  Microchip Atmega
Development Boards:
  Particle Argon
  Arduino BLE
Platforms:
  Particle IO
  Amazon Web Services
  Cisco IoT

## Slide 7: Hardware

## Slide 8: Voltage
Voltage is Potential Energy
Similar to pipe water pressure
All our hardware needs voltage
Common DC voltage levels:
  5 V (max provided by most USB)
  3.3 V (for lower power hardware)
  3 V (coin cell battery)
  1.5 V (AA & AAA battery)
Notes: https://learn.sparkfun.com/tutorials/voltage-current-resistance-and-ohms-law/voltage

## Slide 9: Resistance
Things we power have / need Resistance
Similar to a garden hose faucet
Having no resistance causes short circuit
Your resistance will “spend” your energy
Notes: https://learn.sparkfun.com/tutorials/voltage-current-resistance-and-ohms-law/voltage

## Slide 10: Current
Current is like the water which flows in our garden hose
The base reference that voltage relates to is called ground
We have to “drain” our voltages to ground voltage to get current
GND
(0 V)
GND
(0 V)
5 V
Resistance (powered device)

## Slide 11: Breadboard
Help develop without soldering
Easy swapping of components
Hidden “wires” to connect parts
Slot in pins to make a circuit

## Slide 12: Breadboard
=

## Slide 13: Firmware

## Slide 14: Firmware
Code that directly controls hardware
  Memory, interrupts, data transfer, boot process
Most often programmed in C, but Rust use is growing
Firmware is everywhere!
  BIOS, SSDs, keyboards, IoT devices etc.
To write firmware, you must first understand the hardware
Every processor architecture requires specific firmware
Notes: Firmware: Rust is a programming language similar to C++ but with safe memory management. Its memory features make it ideal for embedded systems. Even the Linux kernel has Rust code!

## Slide 15: Chip Architectures
Texas Instruments MSP430
Microchip/Atmel AVR
IO!
IO!
Notes: Firmware:
The two images are block diagrams of what a chip looks like inside (point to the main controller in the argon).
No need to understand everything in the image. But for example the highlighted circles are registers that control the physical pins on the board.
By saying pinMode() in Arduino we are controlling those ports.

## Slide 16: Embedded C
The same thing as C, but with compiler-specific macros
No libraries, you must read the chip’s documentation!
Texas Instruments MSP430
Microchip/Atmel AVR
Notes: Firmware:
Macros are names/sequence of steps given by the developers to the registers we just saw. So in the AVR image PORTB is controlling the PORTB we saw in the block diagram of the last slide.
Every architecture has different names. If you are an embedded developer, you will typically know a few architectures very well, but will have to read documentation when working with a new chip.

## Slide 17: Firmware Frameworks
Abstract the manual bitwise operations with a header file
The Arduino framework is widely used and works with most chips
Embedded C AVR
Arduino Framework
Notes: Firmware:
No need to address individual macros. The Arduino.h file takes care of everything for you.
If you want to be an embedded systems engineer you MUST program in embedded C, but it is much more forgivable for IoT.
Embedded C provides more bare-metal access to hardware, libraries can sometimes waste space and clock cycles.

## Slide 18: Firmware to Cloud
When working with IoT applications you will typically use frameworks
Particle uses the Arduino framework with added functionality, such as cloud variables and functions
  Cloud variables and functions can be accessed from the web interface!
NuvIoT and Arduino also offer cloud specific libraries for IoT applications
Notes: Firmware:
We’ll show cloud functions in the hands-on!

## Slide 19: Board Setup

## Slide 20: Getting Ready
docs.particle.io/quickstart/argon/
“Set up your Argon”
“Get Started”
Make Account (required)

## Slide 21: Updating
Attach antenna to Argon board “Wi-Fi” port
“Start setting up my device”
Attach board with USB cable to laptop
“Select Device,” pick device, and “connect”
“Continue,” pick device, and “connect”
“Continue” and “Update Device”

## Slide 22: Registering
“Or create a new product” and give a name
“Add to product” and gave a device name
“Name Device”
Choose Wi-Fi network (Not school Wi-Fi, try phone hotspot)
Activate Device
“Go to Console”
Open Web IDE

## Slide 23: Circuit Assembly
3v3 voltage to long leg of LED
GND to short leg of LED

## Slide 24: Coding

## Slide 25: Code – Beginning

## Slide 26: Code - Setup

## Slide 27: Code - Loop

## Slide 28: Code – Functions

## Slide 29: Code – Dashboard Interface
You can now:
Set the clock and timer remotely
Check the current time
Also possible:
Change output to hours & minutes
Using a mobile app to access the dashboard and notifications remotely
More tutorials and code are available at
https://docs.particle.io/getting-started/hardware-tutorials/hardware-examples/